## Slide 1: Ocean WRIT at NOAA/PSL
Tools for mapping, time-series, and spatial correlations ocean reanalyses and observational time-series.
https://psl.noaa.gov/data/writ_new/
Presentation given May 2020.
Additional datasets, variables, and features have been added since.

## Slide 2: Ocean Datasets
Reanalyses | Original horizontal resolution | Original Time range | Original vertical resolution
GODAS | 418x360 | 1979-present | 40 levels
SODA3 | 330x720 | 1980-2017 | 50
ORAS5 | 180x360 (a higher res irregular grid available) | 1979-2018 (some 1958) | 75
EN4 | 173x360 | 1980-2017 | 42
Dataset | Original horizontal resolution | Original Time range | Original vertical resolution
HadISST1.1 | 360x180 | 1870-present | N/A

## Slide 3: Variables
Temperature
Salinity
u, v currents
Heat Content (0-700, 900-1800?)
Bottom Temperature
Momentum flux (u,v)
Depth of the 20 C isotherm (tropics)
Depth of other surfaces, e.g. some density (sigma levels)?
Bottom temperature & salinity
Meridional overturning stream function?
Meridional ocean heat transport
SSH
Sea Surface/Skin Temp
Heat Content (0-300)
Total downward heat flux at surface
Salt Flux
Ocean mixed layer depth
Ocean isothermal layer
To be calculated
Single Level
Depth
Have

## Slide 4: Interpolated Dataset Resolution
Interpolation Method
Data was interpolated at each grid to the vertical levels using a simple linear interpolation
Each level was then interpolated to 1x1 grid using NCL bilinear interpolation
“Missing” latitudes were filled in with missing values so all datasets -89.5 to 89.5
Longitude: 1degree. 0,1,2,3…359
Latitude: 1 degree -89.5,-88.5…88.5,89.5
Vertical: 10, 20, 30, 50, 75, 100, 125, 150, 175, 200, 250, 300, 400, 500, 750, 1000, 1500m

## Slide 5: Ocean WRIT Mapping Page

## Slide 6: GODAS SSH for Jan 2016

## Slide 7: Maps: Returned content

## Slide 8: Map: Jan 2016 SSH: GODAS Mean and Anomaly

## Slide 9: Compare GODAS, SODA3 15m u-current Jan 2016

## Slide 10
Compare GODAS, SODA3 15m u current Jan 2016:
Statistics

## Slide 11
Compare GODAS and ORAS5 Decadal Difference SST

## Slide 12
Compare SODA3,ORAS5 Salinity 0N,200E Mar 2016

## Slide 13
GODAS temperature Mar 2016 1S:1N

## Slide 14: Ocean WRIT Correlation Tools

## Slide 15
AO: Arctic Oscillation R1 (NOAA/CPC) 1950-present
AO: Arctic Oscillation 20CRV2C (NOAA PSL) 1871-present
SOI: Southern Oscillation Index (CRU) 1866-present
Nino 12: HadISST1.1 (NOAA PSL) 1870-presentt
Nino 3 HadISST1.1 (NOAA PSL) 1870-present
Nino 3.4 HadISST1.1 (NOAA PSL) 1870-present
Nino 4 HadISST1.1 (NOAA PSL) 1870-present
MEI Extended (NOAA PSL) 1871-2005
MEI (NOAA PSL) 1950-2018
MEI V2(NOAA PSL) 1979-present
Global Average Land and SST Temperature (NASA) 1880-present
NP: North Pacific Index (NCAR) 1899-present
DMI Dipole mode Index HadISST1.1 (JAMSTEC) 1870-present
NAO: North Atlantic Oscillation (CRU) 1821-present
GBI: Greenland Blocking Index 1851-present",
ALBSA: Aleutian Low and Beaufort Sea Anticyclone (NOAA PSL) 1948-present
PDO: Pacific Decadal Oscillation (U Washington) 1900-present
PDO: Pacific Decadal Oscillation (NOAA PSL) 1891-present
NPGO: North Pacific Gyre Oscillation (U Georgia) 1950-present
AMO: Atlantic Meridional Oscillation (NOAA PSL) 1856-present
QBO: Quasi-biennial Oscillation R1(NOAA PSL) 1948-present
ONI: Oceanic Nino Index (NOAA/CPC) 1950-present
AMM: Atlantic Meridional Mode (U Wisconsin) 1948-present
MM: Pacific Meridional Mode (U Wisconsin) 1948-present
Solar Flux Index 10.7cm (NOAA/NCEI) 1948-present
TNI: Trans Nino Index HadISST1.1 (NOAA PSL) 1870-present
PNA: Pacific North American Index (NOAA/CPC) 1950-present
PNA: Pacific North American Index 20CRV2c (NOAA PSL) 1871-2014
Central Pacific Heat Content (NOAA/CPC) 1979-present
SAM: Southern Annular Mode from 20CRV2c (NOAA PSL) 1851-2011
TPI: Tripole Index HadISST1.1 (CRU) 1870-2015
Sewell Tidal Index (PSL) 1980-2018
Battery Park Tidal Index (PSL) 1856-2018
San Diego Tidal Index (PSL) 1906-2018
Honolulu Tidal Index (PSL) 1905-2018
Kwajalein Tidal Index (PSL) 1946-2018",
Sunspots Monthly Mean (WDC-SILSO) 1749-2017
NH Ice Extent (NSIDC) 1978-present
NH Ice Area (NSIDC) 1978-present
SH Ice Extent (NSIDC) 1978-present
SH Ice Area (NSIDC) 1978-present
Atlantic Hurricane Days (Klotzbach) 1851-2018
Atlantic Hurricane ACE (Klotzbach) 1851-2018
NW Pacific Hurricane Days (Klotzbach) 1950-2018
NW Pacific Hurricane ACE (Klotzbach) 1950-2018
NE Pacific Hurricane Days (Klotzbach) 1971-2018
NE Pacific Hurricane ACE (Klotzbach) 1971-2018
Equatorial C. Pacific Heat Content 160E-80W (NOAA/CPC) 1979-present
N Sierra 8 Station Precipitation Index (CDEC): 1921-present
C Sierra 5 Station Precipitation Index (CDEC): 1921-present
S Sierra 6 Station Precipitation Index (CDEC): 1921-present
Lees Ferry Natural Flow (USBR): 1905-2015
Upper Colorado Basin Temperature (NCEI): 1895-2017
Upper Colorado Basin Precipitation (NCEI): 1895-2017
CO2: Mauna Loa (GMD): 1958-present
CO2: Global Average (GMD): 1980-present
Trend
Available Time-series

## Slide 16
Map of Correlations: EN4 SST and 3.4

## Slide 17
Correlation Jan SSH and San Diego Tidal Time-series

## Slide 18
NPGO Time-series correlated with Jan GODAS SSH and v-current

## Slide 19
Correlation Nino 1.2 with Jan SODA temperature: Color-Scale Change

## Slide 20: Correlation Nino3.4 3 vs 6 month lead SST

## Slide 21
Trend of GODAS Mar Surface Heat Flux

## Slide 22: Top Panel from: Cook, K.H., Vizy, E.K. & Sun, X. Multidecadal-scale adjustment of the ocean mixed layer heat budget in the tropics: examining ocean reanalyses. Clim Dyn 50, 1513–1532 (2018). https://doi.org/10.1007/s00382-017-3703-0
U-current: lat/depth for GODAS annual mean and trend

## Slide 23: Ocean WRIT Time-series

## Slide 24
Time-series: Mixed Layer Depth GODAS 0N,200E

## Slide 25
Time-series: Salinity 50m ORAS5 vs SODA3 0N,200E

## Slide 26
Time-series: Winter Temp vs u current 0N,200E

## Slide 27
Scatter Plot: Winter Temp vs u current 0N,200E

## Slide 28
Pre-generated Time-series

## Slide 29
Wavelet Analysis: Sewell Tidal Gauge

## Slide 30
Add more datasets
Improve plots
Add lead/lag for timeseries
Calculate more variables
Add years for datasets that are updated (GODAS)
Add SST or SLP or other observational datasets
Consider add coupled variables
Obtain more ‘ocean’ timeseries. Fish? Plankton?
Add biological datasets
Future